## Slide 1
-Enable RSTP
-Configure BPDUGuard and PortFast on PCs interfaces.
-Configure S1 as VTPv2 server domain: CCNA255N
-Configure S2 &S3 as VTPv2 clients
-Configure R2 for VL10-12, VL20-21 (Last IP as GW)
-Configure R3 for VL22, VL30-32, VL99 (Last IP as GW)
-Configure S1,S2,S3 with SVI for VL99 where 10.99.99.X=S#
-Configure S1 for routing, create routed ports for f1/0/1-2 but only put an ip address on f1/0/1 from 10.10.10.8
-Configure R1 interface G0/1 with an ip address for the 10.10.10.8/30 network
-Enable Remote access on all devices
-Enable Web Services on R1; ensure you can access the web server via http://x.x.x.x
-Ensure S1 is primary root for VL10-12, VL20-21 and secondary for VL22, VL30-32, VL99
-Ensure S2 is primary for VL22, VL30-32, VL99 and secondary root for VL10-12, VL20-21
VLAN # | VLAN Name | IP Space
VLAN10 | DATA1 | 172.16.10.0/24
VLAN11 | VOICE1 | 172.16.11.0/24
VLAN12 | IT | 172.16.12.0/24
VLAN20 | DATA2 | 192.168.20.0/24
VLAN21 | VOICE2 | 192.168.21.0/24
VLAN22 | Research | 192.168.22.0/24
VLAN30 | DATA3 | 10.0.30.0/24
VLAN31 | VOICE3 | 10.0.31.0/24
VLAN32 | HR | 10.0.32.0/24
VLAN99 | MGMT | 10.99.99.0/25
R1
R2
R3
S2
PC1
VL10
PC2
VL20
PC3
VL30
S0/0
S0/0
S0/1
S0/1
G0/0
G0/0
F1/0/5
F0/5
F1/0/1
F1/0/2
G0/0
G0/1
F1/0/6
F1/0/3
F1/0/4
F0/3
F0/4
F0/7
F0/8
F0/7
F0/8
F0/6
OSPF Area 0
L1-1.1.1.1
L1-2.2.2.2
L1-3.3.3.3
Internet
L0-209.165.100.100
10.10.10.0/30
10.10.10.4/30
10.10.10.8/30
L3 Mode On Only
F0/6
S3
S1
F1/0/10
F1/0/11
F0/10
F0/11
PAgP
LACP
LACP or
PAgP
-Configure PAgP between S1 & S3.
-Configure LACP between S2 & S3.
-Configure either Protocol between S1 & S2
-Configure L3 Ether channel mode ON from R1 to S1.
-Propagate default route from R1 to all routers.
-Configure HSRP for VL10,20, & 30.
-Ensure HSRP work for VL10,20 & 30 PCs.
-Configure Multi-area OSPF where VL11-12 is in Area 2, VL22, VL31-32 is in Area 3, and all other networks in Area 0.
-Ensure Router IDs are loopback 1 address.
-Set bandwidth on all Serial interfaces to 1.544Mbps

## Slide 2
-Configure R2 for VL10-12, VL20-21 (first IP as GW)
-Configure R3 for VL22, VL30-32 (first IP as GW)
-Configure R3 for VL 99 (2001:10:99:99::99 as the GW)
-Configure S1,S2,S3 with SVI for VL99 where 2001:10:99:99::X=S#
-Configure S1 for ipv6 routing, create routed ports for f1/0/1-2.
-Enable Remote access on all devices
-Enable Web Services on R1; ensure you can access the web server via http://x.x.x.x
-Configure L3 Etherchannel mode ON from R1 to S1
using ipv6 network address above.
-Propagate an ipv6 default route from R1 to all routers.
-Configure EIGRP for IPV6.
-Ensure PC1, PC2, and PC3 can ping each other, Internet IPv6, Router Loopbacks, and Ipv6 address on switches.
VLAN # | VLAN Name | IP Space
VLAN10 | DATA1 | 2001:172:16:10::/64
VLAN11 | VOICE1 | 2001:172:16:11::/64
VLAN12 | IT | 2001:172:16:12::/64
VLAN20 | DATA2 | 2001:192:168:20::/64
VLAN21 | VOICE2 | 2001:192:168:21::/64
VLAN22 | Research | 2001:192:168:22::/64
VLAN30 | DATA3 | 2001:10:0:30::/64
VLAN31 | VOICE3 | 2001:10:0:31::/64
VLAN32 | HR | 2001:10:0:32::/64
VLAN99 | MGMT | 2001:10:99:99::/64
R1
R2
R3
S2
PC1
VL10
PC2
VL20
PC3
VL30
S0/0
S0/0
S0/1
S0/1
G0/0
G0/0
F1/0/5
F0/5
F1/0/1
F1/0/2
G0/0
G0/1
F1/0/6
F1/0/3
F1/0/4
F0/3
F0/4
F0/7
F0/8
F0/7
F0/8
F0/6
IPv6 EIGRP AS 100
L1-2001:1:1:1::1
L1-2001:2:2:2::2
L1-2001:3:3:3::3
Internet
L0-2001:209:165:100::100
2001:10:10:12::/64
F0/6
S3
S1
F1/0/10
F1/0/11
F0/10
F0/11
PAgP
LACP
LACP or
PAgP
2001:10:10:13::/64
2001:10:10:11::/64
L3 Mode On Only